ASSERT:

(post of the representative of the organization)

_____________ I.I.Ivanov

"_____" __________________ 2005.

T A S K

on development of the equipment design «The hen house on 1 million broilers with a greenhouse-roof «The pendant gardens of Semiramida» under the contract № _________ from _____________ 2005.

| № п/п | The list of the basic data and requirements | The contents of the basic data and requirements |
| --- | --- | --- |
| 1 | 2 | 3 |
| 1. | The name of the project | The hen house on 1 million broilers with a greenhouse-roof «The pendant gardens of Semiramida» |
| 2. | The basis for designing |  |
| 3. | The organization which is carrying out functions of the customer |  |
| 4. | A source of financing |  |
| 5. | The general design organization | Research and a project institute On creation city and industrial complexes, Objects of cultivation, storage and processing Fruit-and-vegetable production RPI «GRADOAGROECOPROM» - Licenses of the state committee of the Russian Federation on construction and a housing-and-municipal complex Д 233247 ГС-1-50-02-26-0-7710134192-017306-1, Д 233248 ГС-1-50-02-27-0-7710134192-017307-1 and Д 233249 ГС-1-50-02-28-0-7710134192-017308-1 Are valid for 24.05.2005, - The certificate of an estimation of the rights to "KNOW-HOW" № 00486 series АА № 00НХ 486 class 00НХА 20В1, is valid on January, 01, 2010. |
| 6. | Stages of the development | The equipment design. In one stage. |
| 7. | Terms of representation on consideration and the statement | According to the planned schedule. |
| 8. | Asserting instance |  |
| 9. | The purpose of object, its basic characteristics hen house greenhouses | 1) the Hen house is intended for cultivation of broilers. Capacity of one hen house 1 million heads. 2) The greenhouse is intended for cultivation of vegetables by the method of multistoreyed narrowshelving hydroponics |
| 10. | Requirements to technology and the organizations of manufacture hen house 2) greenhouses | Cultivation of broilers on a hen house is made all-the-year-round. The daily young growth acts from breeding reproducers and is raised up to 9-week age. For heating chickens on a hen house запроектировать pendant brooders with vacuum drinking bowls and groove feeding troughs. In other part of hen houses mechanization of processes to solve on the basis of the complete set of equipment ЦБК-18 with the limited feeding. Cultivation of a bird is carried out on a deep laying at artificial illumination with a light mode adjustable on the set program. In a greenhouse to provide branch сеянцев, рассадное and vegetable branch. Cultivation of vegetables to make in polyethylene pots, cultivation seedlings - in cartridges on 16 cells. Solution units and rooms for stuffing pots and cartridges to place on 1 floor in the block with a hen house. |
| 11. | Requirements to architectural, space-planning and constructive decisions hen house 2) greenhouse | 1. To accept the walls of the hen house made from the facilitated fireproof panels such as «Sandwich», the bases and a column ferro-concrete. Internal furnish - waterproof painting. 2. To accept as carrying modular designs of a frame of the greenhouse for accommodation of hydroponic trays with the sizes in axes of 2,1 m; a step of frames - 1,5 m. Protection of the greenhouse to execute from a glass on aluminium panels. Partitions of the greenhouses and carrying designs is the steel zinced structures of factory manufacturing. |
| 12. | Technology requirements to engineering systems hen house greenhouses | To project the internal engineering equipment of hen houses according to requirements of norms. To provide a forced-air and exhaust ventilation, water supply, electro supply, heat supply, the water drain, the fire signal system. In the greenhouse to provide: On systems of water supply and water removal: Solution units such as SIMNH; System of preparation and top dressing by mineral fertilizers. On systems of heating: Heating in branch сеянцев, рассадном and vegetable to execute system of roofing heating (heating pipes for heating air place under a roof) - the heat-carrier water with Т = 130-700С, system above the ground warmed the heat-carrier water with Т = 95-700С, system above the roof heating - the heat-carrier water with Т = 40-300С; - Pipes of system of heating to accept in accordance with GOST 10704-91 and GOST 3262-75. On systems of addition lighting: - Irradiating installations УОРТ 15-400-ДнаТ; УОРТ 24-250-ДнаТ. |
| 13. | Requirements to mechanization and automation of productions in a greenhouse | To provide the mechanization of productions and automation of maintenance of a microclimate and meal of plants in the greenhouse and light mode in hen house. |
| 14. | Conditions of electro supply, a heat supply, water supply of the household water drain, installation of telephones and installation of wired radio units | -Electro supply from an external source, a category of manufacture on reliability of electro supply II and III. -Heat supply - from own boiler-house with parameters of the heat-carrier - water 130-700С, a category on reliability II. -Water supply from an external source. -Water removal - in external networks of the water drain. -To provide installation of telephones and installation of wired radio units. |
| 15. | Requirements and conditions to development of nature protection measures and actions | According to working normative documents |
| 16. | Requirements to a mode of safety | According to working normative documents. |
| 17. | Requirements on development of engineering - technological actions of a civil defence and actions under the prevention of extreme situations | Are not developed |
| 18. | Requirements on performance of developmental, research works | According to the program |
| 19. | Conditions of construction and operation | The project to develop for area with: - In settlement temperature of external air of the coldest day a minus 350С; -In weight of a snow cover for greenhouses of 15 kgs/m2 it agrees СНиП 2.10.04-85 and for massive buildings - 126 kgs/m2; - Normative values of wind pressure - 38 кгs/m2; - Seismicity no more than 6 points. Temperature-moist mode in the greenhouse on НТП 10-95. |
| 20. | The basic technical and economic parameters | The quantity of floors - 2. The general area of a building - 1720 m2 The general area of building - 1773,8 m2 General budget cost - 94758,37 thousand roubles. Including greenhouses - 56671,37 thousand roubles. Hen house - 38087,00 thousand roubles. Cost of 1 m2 - 53,42 thousand roubles. Including greenhouses - 32,95 thousand roubles. Hen house - 20,73 thousand roubles. The area of a greenhouse - 1720 m2 The area of branch seedlings - 86 m2 The area of seedling branch - 300 m2 The area of vegetable branch - 1342 m2 The output of О2 from one sq. decimeter of a sheet surface at one o'clock - 20 mg / сј2 at one hour. Productivity - 120-150 kg / m2 one year Need of plants in СО2 - 6 g/m2/hour. As a substratum riding peat is used. |
| 21. | Requirements to quality, competitiveness and ecological parameters | Production should be: high-quality, non-polluting and safe for health of the person, and also competitive Russia in a home market. The quantity of nitrates at 8-10 times is lower than maximum concentration limit. |
| 22. | Requirements on development of variants of design decisions | Do not to develop. |
| 23. | Perspective expansion of the enterprise | Do not to provide |
| 24. | Introduction of advanced achievements of a science, technical equipment and the best practices | Development is carried out at a level of the best world samples and assumes realization of the patented ways of maintenance of buildings by oxygen and cultivation of plants by method MNH, application of the patented designs of greenhouses, engineering and the process equipment, and as patented modes of operation of an industrial zone. |
| 25. | Patent protection of a standard project | A way of cultivation of plants, sprouts and seedlings by the method of MNH. |
| 26. | Licensors | RPI «Gradoagroecoprom» |
| 27. | Conditions of definition of cost of construction | Estimates to make according to methodical instructions by definition of cost of production in territory of the Russian Federation in the current prices. |
| 28. | Special conditions of development of the project | Units of regulation of temperature, power boards, boards of automatics and solution units to place on a ground floor. To develop drawings of the necessary not standardized equipment. To develop technical requirements on the device of automatic control of a microclimate and a feed of plants in a hen house and a greenhouse. The steel zinced both aluminium structures and designs from them to develop with reference to technology. |

Appendices:

- Patents for the inventions used by development of the project.

- Culture circles at cultivation of vegetables and manufacture of oxygen by method MNH.

COORDINATED:

Director RPI «Gradoagroecoprom»                      					 V.P.Sharupich